## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – SIH26126
Problem Statement Title- Vision Based Autonomous Navigation for Unmanned Ground Vehicle for Outdoor Environment
Theme- Smart Automation
PS Category- Software
Team ID- 125626
Team Name- Innopath

## Slide 2: VISION-FIRST AUTONOMOUS UGV FOR GPS-DENIED OUTDOOR NAVIGATION
PROBLEM
GPS unreliable in forests, hills and disaster zones
LiDAR-heavy UGVs are costly and power-hungry
Unstructured terrain has no lanes or fixed map
Lighting, shadows, dust change what the camera sees
Moving obstacles need real-time replanning
KEY GAP
Low-cost navigation that needs no GPS and no prior map
PROPOSED SOLUTION
RGB Camera + IMU
Perception AI
Visual Localization
Dynamic Planning
Safe Navigation
OUR SOLUTION
Camera-first: one RGB camera is the primary sensor
Perception: lightweight AI marks traversable ground and obstacles
Localization: visual odometry + SLAM give pose and a local map, no GPS
Planning: global + local planner replans around moving obstacles
Control: ESP32 turns path into motor commands
WHAT MAKES IT DIFFERENT?
01 Vision-first
one camera, no LiDAR
02 GPS-independent
no prior map needed
03 Lightweight
real-time on edge hardware
04 Low-cost & portable
fits different UGV platforms

## Slide 3: TECHNICAL APPROACH
TECHNOLOGIES TO BE USED
01 | Camera + IMU
Sensing and motion cues
02 | Python + PyTorch
Model training, inference
03 | OpenCV
Image processing
04 | Lightweight AI model
Terrain + obstacle segmentation
05 | Visual Odometry
Frame-to-frame motion
06 | Visual SLAM
Pose + local map
07 | A* / Dijkstra planner
Global + local paths
08 | Onboard edge computer
Runs the full stack
09 | ESP32
Low-level motor control
METHODOLOGY: SYSTEM FLOW CHART
1 SENSE
RGB camera
IMU
2 PERCEIVE
Lightweight AI
Traversable ground
Obstacles
3 LOCALIZE
Visual odometry
Visual SLAM
Local map
4 PLAN
Global planner
Local replanning
5 ACT
ESP32 controller
Motor commands
UGV moves
Feedback loop: new camera frames update the map and the path continuously
IMPLEMENTATION PROCESS

## Slide 4: FEASIBILITY AND VIABILITY
ANALYSIS OF FEASIBILITY
Public outdoor datasets
AI training
Simulation
Software validation
Low-cost UGV prototype
Software-first: the perception and navigation stack is proven in software before any hardware risk is taken
Accessible parts: camera, IMU, edge computer and ESP32 are all commodity, low-cost components
POTENTIAL CHALLENGES AND RISKS → STRATEGIES TO OVERCOME
Changing illumination
Diverse training data
Unseen terrain
Testing on unseen environments
Limited computing resources / real-time inference
Lightweight model optimization
GPS-denied operation, visual localization drift
Visual-inertial fusion (camera + IMU)
Dynamic obstacles
Local dynamic replanning
Risk in physical trials
Simulation before physical deployment

## Slide 5: IMPACT AND BENEFITS
POTENTIAL IMPACT ON THE TARGET AUDIENCE
AUTONOMOUS UGV
SEARCH & RESCUE
GPS-denied environments
Keeps responders out of hazardous ground
AGRICULTURE
Unstructured terrain
Navigates farm land with no fixed lanes
DELIVERY
Outdoor environments
Moves goods over paths without GPS
BENEFITS OF THE SOLUTION
OPERATIONAL
Reduced dependence on GPS
OPERATIONAL
Autonomous operation in unstructured terrain
ECONOMIC
Lower-cost, vision-first navigation
ECONOMIC
Deployable on different UGV platforms
SOCIAL
Reduced manual intervention and human exposure

## Slide 6: RESEARCH AND REFERENCES
1. OFF-ROAD DATASET — RELLIS-3D
Why we use it:
Off-road scenes with terrain labels to train and test traversability perception.
Reference:
Jiang et al., RELLIS-3D Dataset: Data, Benchmarks and Analysis, ICRA 2021 (arXiv:2011.12954)Link
2. OUTDOOR DATASET — GREAT OUTDOORS
Why we use it:
Additional outdoor imagery for diverse-terrain training and unseen-environment tests.
Reference:
The Great Outdoors Dataset
3. BENCHMARK — KITTI
Why we use it:
Standard benchmark to check visual odometry and localization drift.
Reference:
Geiger, Lenz, Urtasun, Are we ready for autonomous driving? The KITTI vision benchmark suite, CVPR 2012Link
4. VISUAL SLAM — ORB-SLAM3
Why we use it:
Reference for camera-based (and visual-inertial) localization and mapping.
Reference:
Campos et al., ORB-SLAM3, IEEE Trans. Robotics 37(6), 2021 (arXiv:2007.11898Link
5. LIGHT PERCEPTION — MobileNetV3
Why we use it:
Basis for a small, fast backbone that runs in real time on edge hardware.
Reference:
Howard et al., Searching for MobileNetV3, ICCV 2019 (arXiv:1905.02244)Link
6. EXISTING vs OUR CONTRIBUTION
Existing:
Autonomous UGVs, visual SLAM and terrain segmentation are established.
Our contribution:
One integrated, lightweight, vision-only GPS-denied pipeline on low-cost hardware, tested on unseen outdoor terrain.
Source: Official problem statement